# Multimedia and Hypermedia Programme Stream Format for 6G (MP6)
## Design Goals
MP6 is designed to be a container format, optimized for network transfers. Consequently, it is made compact. In particular, no indexing. Implementations are free to generate indexes, of course, but they are not part of this memo. Also, no DRM.
MP6 is also intended to be flexible enough, covering a wide range of uses. As a degenerate case, it is a container of HTML static objects in a help system.
## Terminology
Static Object (SO) is a piece of data not associated with a timeline. Semantically, it could be meta-data (not part of an ES), add-on, or content such as a menu.
SO consists of MIME type, name (MUST be short; 2 letters are enough for most cases), and actual content.
Elementary Stream (ES) is a syntactical and semantical unit of MP6.
All ES in an MP6 file form a single programme, so they belong to one timeline.
All MP6 content is either SO or ES. Each file consists of 0 to many SO, and 0 to many ES.
Each ES has a type.
Just 6 types, so 3 bits are enough. How many ES of given type? 6 bits.
Although MP6 defines planes for ES, they are not substreams.
Up to 8 planes, so 3 bits.
SYNCPOINT (SNCP) is a part of the timeline.
Frame: this term is intentionally not used for its ambiguity.
Elementary Data Unit (EDU) is the basic building block of MP6. Each EDU is either SO, or a part of an ES (associated with a plane) (ESDU), or a SNCP.
## Encoding
Magic number: “MP6” followed by 1-byte version number (binary). For this specification the version is 0h. Everything else is EDU encoded as chunks; each chunk consists of 16 bits size in bytes (of its data, not including these 16 bits) + data, as following. 2 MSBs of data in a chunk define its type: 00 → SO, 01 → ESDU, 10 → SNCP, 11 → reserved (remix pack?).
## SO Encoding
Byte 1: 00|6 bits of name length. The name MUST be short; 2 bytes should be enough for most implementations.
Bytes [2...n]: name of the SO.
Bytes [n+1...m]: MIME type of the SO. TODO: compress the major type into 1 byte?
Byte m+1: “;” as a separator
Bytes [m+2...]: actual data.
## ESDU Encoding
Byte 0: 01|ppp|ttt, where ppp=plane, ttt=type of the ES. Type and number uniquely define the ES.
Byte 1: number of the ES. Numbers are type-specific.
Bytes 2...: data.
## SNCP Encoding
Byte 0: 10|duration (most significant). Duration is measured in 100 ns from the previous SNCP or the beginning of the file.
Byte 1: duration (least significant).
Byte 2: flags.
Bit 0: Key frame (all ES'es), applies to the portion before.
## Planes
0: content
1: meta-data; format (ES type specific)
2: video: palette; not used otherwise
3: language (natural, alpha-2)
4: ES name (better, use file meta-data)
## Video (ES Type 0)
Define format (GUID),
frame size (2x2 bytes),
aspect ratio (2 bytes) (4:3 → 1333, 16:9 → 1778, 2.35:1 → 2350),
flags (1 byte: 3D, interlacing, K frames),
Format specific
## Audio (ES Type 1)
Plane 1 is: GUID,
sample rate (2 bytes, in 10Hz; examples in Hz: 8000, 11025, 22050, 44100, 48000, 96000)
no. of channels (1 byte; bit 7=flag for subwoofer)
bits per sample (1 byte, valid 8, 16, 4)
extra (format specific).
## Subtitle (ES Type 2)
Text. No plane 1.
## Command (ES Type 3)
Format: GUID. For example, see MHEG-1, MHEG-5.
## Text/teletext (ES Type 4)
Format: GUID
## Sub-picture (ES Type 5)
Same format as Video.
# All ES Types
Video → 0
Audio → 1
Teletext (WST) → 4
Subtitles → 2
Guide → not supported (or SO)
Built-in tables → N/A
Big packets → N/A
Interactive, feedback (as MHEG-5, DSM-CC) → SO or 3
Menu → SO
Scene description → SO
Sub-picture → 5
Synchronization (SMIL etc) → SO
# MCF (Pre-Matröška)
0=Control
 TOP-atom: Jump IfEd ChEd Enab Disa Quit Menu AltO Link
 MENU-atom: Stop Loop Pict Tout Area
 AREA-atom: Shap Left Hili Acti
 SHAPE-atom: Rect Poly Circ
 HILI-atom: Pict Soun Link
1=Video
DB Flags (Interlaced, 3D)
DB 0
DW X
DW Y
DW Aspect (4:3 → 1333, 16:9 → 1778, 2.35:1 → 2350)
FOURCC
DD Colorspace (~AVI)
GUID
DB Gamma
2=Audio
DD Sample rate (mHz)
DB Bit depth
DB flags (S/PDIF; Secondary)
DB subtracks (languages)
DB channels / subtrack
DW wFormatTag
DD Channel positioning (…)
SubTrack:
Language 64 bytes
ISRC 12 bytes
reserved 4 bytes
3=AV
10h=Titles
Picture in Rect.
11h=Subtitles
charset (0=UTF8), colour (4: R8G8B8), flags (black-bg, top)
In text: control codes (switch colour, bold, underline, italics; karaoke timing)
Karaoke in fraction (0 – 255) per frame.
# MCF Channel Mapping
#define SPEAKER_FRONT_LEFT 0x1
#define SPEAKER_FRONT_RIGHT 0x2
#define SPEAKER_FRONT_CENTER 0x4
#define SPEAKER_LOW_FREQUENCY 0x8
#define SPEAKER_BACK_LEFT 0x10
#define SPEAKER_BACK_RIGHT 0x20
#define SPEAKER_FRONT_LEFT_OF_CENTER 0x40
#define SPEAKER_FRONT_RIGHT_OF_CENTER 0x80
#define SPEAKER_BACK_CENTER 0x100
#define SPEAKER_SIDE_LEFT 0x200
#define SPEAKER_SIDE_RIGHT 0x400
#define SPEAKER_TOP_CENTER 0x800
#define SPEAKER_TOP_FRONT_LEFT 0x1000
#define SPEAKER_TOP_FRONT_CENTER 0x2000
#define SPEAKER_TOP_FRONT_RIGHT 0x4000
#define SPEAKER_TOP_BACK_LEFT 0x8000
#define SPEAKER_TOP_BACK_CENTER 0x10000
#define SPEAKER_TOP_BACK_RIGHT 0x20000